# WEXNER CENTER FOR THE ARTS

LOADING AND UNLOADING		the Wexner Center has a centrally located dock, which has

three main bays.  Two bays have hand-operated mechanical

leveler plates.  Bay doors measure 10’-0” x 12’- 0”.  Access

to the Mershon stage is through the stage right wing which

is on the dock level.  Access to the Performance Space, 						Weigel Hall, and Exhibition galleries is by means of a freight

elevator, which measures 8’-0” x 9’-0” x 16’-0” with a

weight capacity of 10,000 pounds.

PARKING				Parking is available for trucks and buses in the loading dock

ramp or upper service road.  Overnight parking must be

arranged in advance.  Shore powering for vehicles is avail-

able on a three phase 200 amp disconnect located in the dock

area.  This also must be arranged in advance.

# PERFORMANCE SPACE THEATER

STAGE DIMENSIONS			The usable floor space can best be described as a trapezoid

lying within the boundaries of the balcony.  The north wall

is 45’-6” in length.  This wall holds the bi part traveler of

black velour, opening and revealing the cyclorama.  The

west side is 40’-0” in length and the east side is 45’-6” in

length.  Both are perpendicular to the north wall.  The south

side is 46’-6” in length and lies at an angle of 12 1/4 degrees

due south of the north wall plane.   (see attached plan)

STAGE FLOOR				The usable performance area and the area under the south

and west balcony is a resilient floor of maple.

The off stage space under the east balcony flooring is of oak

and non-sprung.  Black Marley flooring is available.  Five

rolls at 5’-3” x 45’-6” and one roll at 5’-3” x 37’-3”that

covers upstage of the traveler.

SEATING				Seating is facilitated through the use of four mobile riser

units.  The units are 4’-0” high and 10’-0” wide.  The top

level is 4’-3” in depth and there are five levels of 2’-9” that

pull out, plus one loose unit at 2’-9”.  The height of each of

these levels is 6 1/2”.  The maximum depth fully extended is

20’-11”.  Allowing for aisle, there are four chairs per level

and seating can be arranged on the floor in front of the units.

Side and back safety railings are available.

GRID AND HANGING			The upper structure at 24’-3” underpassage is comprised of

POSITIONS				a cat walk system with hanging positions at 28’-8” from the

deck.  The north end of the grid is an aircraft wire mesh

system which can be walked on.

Five dead-hung pipes are hung at 23’-4” from the deck and

spaced downstage from the traveler and parallel to the north

wall at 1’-2”, 3’-6”, 6’-10”, 8’-8”, and 21’-8”.

RIGGING				The Performance Space has twelve cable winder motors

located in the catwalks that can hit points throughout 							the space and can do preset moves for flying pieces.

The primary use of these winders is normally dedicated to

electric pipe travel.  A hemp sheave system is available,

although it is limited.

STAGE DRAPES			There are 13 pieces of black velour that mask under the

edge of the under balcony.  One two-part black traveler

that measures 46’-0” in width, five black border sections

at 4’-0” x 10’-0”, two sets of legs 8’-0” x 23’-0”, one

black scrim 23’-0” x 37’-0”, and one white bounce.

DRESSING ROOMS	Dressing rooms are available as one common area for production mgr with phones and internet access. Two divided areas male and female with sinks, showers, lockers and makeup tables in each area. Coffee and refrigerator available.

LIGHTING EQUIPMENT		The lighting inventory consists of :

See Current Listing in lighting document.

Other Fixtures via rental.

30	6x16		1000w  FEL

30	6x12		  750w  EHG

12	6x9		  750w  EHG

24	8” Fresnel	1000w  BVV

12	6” Fresnel	  750w  BTN

24	Par Can		1000w  PAR 64

6	14” Scoop	1500w

12	Berkey Far Cyc	1000w

4	Ianebeams 	2000w (worklights)

Source four Lekos avail on request

POWER					1100amps available.  No disconnect for road equipment.

LIGHTING CONTROL	The Performance Space lighting console is a Strand 520i. This is a full memory console with 250 control channels.  The lighting control booth is located above the balcony on the east wall and allows for a view of  70 % of the stage area. Or operation may be in a designated tech area in the balcony.

DIMMERS	The dimmers are Strand  CDX80. The system is DMX. There are 6 dimmers at 6000 watt and 168 dimmers at 2400 watts. Pared circuits are located throughout the space, the grid, the balcony, and under the balcony on the main floor.